## Slide 1: Update: Tacoma PM2.5 Attainment
May 10, 2013
Andrew Green

## Slide 5: What are “wood burning devices”?

## Slide 6: Number of Devices
2008 | Households w/ device | Households that use device
Fireplaces | 30,900 | 21,200
Uncertified inserts and stoves | 24,200 | 21,200
Certified inserts and stoves | 20,200 | 17,200
Pellet stoves | 3,900 | 2,100
Total | 79,200 | 61,700

## Slide 7
Location of wood stoves in Smoke Reduction Zone

## Slide 9: PM2.5 Wood Smoke Emissions
Chart: 
| Fireplaces | Uncertified Inserts | Certified Inserts, non-cat | Certified Inserts, cat | Uncertified wood stoves | Certified wood stoves, non-cat | Certified wood stoves, cat | Pellet Stoves | Firelogs
PM2.5, TPY | 244 | 78 | 63 | 59 | 540 | 53 | 151 | 2 | 14

## Slide 10: Stakeholder Task Force Solutions
Enhanced enforcement of burn bans
Removal of old “uncertified” wood stoves and inserts
  September 30, 2015
Public education and outreach
Support planned reductions from other sources
  E.g. federal engine & fuel standards

## Slide 11
Reduction from each strategy in micrograms per cubic meter (µg/m3)

## Slide 12: Burn Bans

## Slide 13: Enhanced Burn Ban Enforcement
Lower Stage 1 forecast trigger
Significant increase in patrolling staff
  From ~8 to 77
  Interlocal agreements
  1,500 NOVs
Nighttime enforcement
  Most burning happens in evenings
  Long exposure photography
Civil penalty structure
  Initial penalty is $1,000
  Can “get to zero” on first offense, if take action
    e.g. sign up for text alerts, wood stove replacement/removal program
No other adequate source of heat exemption process

## Slide 15: Wood stove program
Three components:
  Low-income replacement (fully funded)
  “Early adopter” replacement incentives
  Removal (buy-back)
  Fireplace pilot

## Slide 16: Wood stove program (cont.)
Low-Income
  Free replacement (allows certified wood)
  157 to date (Apr. 30)
  80 chose wood, 31 heat pump, 23 gas, 18 pellet, 4 propane
Replacement Incentives
  90 to date
    8 “grand prize” free
    88 x $1500/$1000 off new device (no wood)
  Drawings Nov. 30 & Mar. 12
Buy-back / Recycling Reward
  20 x $200 in-home removals to date
  128 x $350 drop-offs to date

## Slide 17: Public outreach
Public outreach a core value and essential to success
Three primary messages
  Burn ban enforcement is increasing. Avoid possible fines.
  Assistance is available to help you “leave your old flame behind.”
  Whenever you burn, practice cleaner burning techniques.
Major public communications campaign
  Multi-media approach
  November 2012-March 2013
www.airsafepiercecounty.org

## Slide 18: Campaign components
Outdoor advertising
Print advertising
Web
  www.airsafepiercecounty.org
  Online advertising
Printed materials (e.g., posters, flyers, fast fact cards)
Targeted direct mail
Regular press
Social media (Twitter, Facebook, YouTube)
Coordinated outreach through local partners

## Slide 20: Questions?
Andrew Green
Puget Sound Clean Air Agency
206-689-4053
AndrewG@pscleanair.org